## Slide 1: A critical review of energy scenarios in Vietnam
VEAM 2019
A work by TRAN Hoang Anh (VIET/USTH) et al.
Presenter: NGUYEN Trinh Hoang Anh (VIET/USTH)
Vietnam Initiative for Energy Transition (VIET)
University of Science & Technology of Hanoi (USTH)
Dalat, 17 June 2019

## Slide 2
Current situation of Vietnam
Electricity generation
Source: Vietnam Electricity Annual Report 2017 - EVN
Important share of coal

## Slide 3: Installed capacity in 2017

## Slide 5
Current situation of Vietnam vs France
CO2 emission in Vietnam
Increase 4 times from 2000 to 2014
Source: World Bank
CO2 emission in France
Decreasing tendency from 2000 to 2017
Major commitment to nuclear energy
Source: https://www.statista.com/statistics/449698/co2-emissions-france/

## Slide 6
Reviewed and comparision of energy studies
10 studies – 24 scenarios
2011
2015
2016
2017
2018
PDP 7
REDS
PDP 7 Rev
PDP = Power Development Plan
REDS = Renewable Energy Development Strategy

## Slide 7: Indicators for the scenario comparison and data availabilities
N. | Report/ Scenarios | PDP 7 (2011) [2] | REDS (2015) [11] | PDP 7R (2016) [4] | IES (2016) [5] | WWF (2016) [12] | MOIT (2017) [13] | GreenID (2017) [7] | ADB (2017) [8] | Danish Energy Agency (2017) [9] | Decision Ware Group & IE (2018) [10]
 | Modelling tools |  |  | Simple-E STRATEGIST – PDPAT II PSS/ADAPT PSSE | Simple-E Corrective – Module 1 | PROPHET electricity planning | BALMOREL | MARKAL | EFFECT The computable general equilibrium (CGE) | BALMOREL | TIMES
 | Approach |  |  |  | Linear programming | Mixed integer programming Least cost investment | Top – down (Partial equilibrium) Least cost optimization | Bottom – up Least cost optimization | Bottom – up GHG emissions forecast model | Top – down (Partial equilibrium) Least cost optimization | Bottom – up Least cost optimization
A | Assumptions |  |  |  |  |  |  |  |  |  | 
A.1 | Population growth projections |  |  |  |  |  |  |  |  |  | 
A.2 | GDP growth |  |  |  |  |  |  |  |  |  | 
A.3 | Energy/power demand forecast |  |  |  |  |  |  |  |  |  | 
A.4 | Energy supply |  |  |  |  |  |  |  |  |  | 
A.5 | Energy efficiency |  |  |  |  |  |  |  |  |  | 
A.6 | Generation technology costs |  |  |  |  |  |  |  |  |  | 
A.7 | Fuels’ cost projections |  |  |  |  |  |  |  |  |  | 
A.8 | Energy policy assumptions | Electricity Law, Oil and Gas Law, Energy Efficiency Law, VNEEP, Coal/Gas Master Plan, RE Strategy | Renewable Energy strategies, Power Master plan | Electricity Law, Oil and Gas Law, Energy Efficiency Law, Energy Strategy to 2050, VNEEP, Coal/Gas Master Plan, RE Strategy | Electricity Law, Oil and Gas Law, Energy Efficiency Law, Energy Strategy to 2050, VNEEP, Coal/Gas Master Plan, RE Strategy | Renewable Energy strategies, Power Master plan, Energy efficiency program | Electricity Law, Oil and Gas Law, Energy Efficiency Law, Energy Strategy to 2050, VNEEP, Coal/Gas Master Plan, RE Strategy | Renewable Energy strategies, Power Master plan, Energy efficiency program | Low carbon policy, GHG emission, NDC target, green growth policies | RE strategy, Carbon price (average and high), Carbon cap, no coal | VNEEP, Coal/Gas Master Plan, RE Strategy, NDC-2 Review and Update of Viet Nam's Nationally Determined Contribution for Energy Sector
A.9 | Carbon price |  |  |  |  |  |  |  |  |  | 
A.10 | Scale (national, regional) | Regional and National | National | Regional and National | National | National | National | Regional | National | National | Regional and National
R | Simulation results |  |  |  |  |  |  |  |  |  | 
R.1 | (Total) Generation mix/ Capacity mix |  |  |  |  |  |  |  |  |  | 
R.2 | Installed coal capacity (in 2030) |  |  |  |  |  |  |  |  |  | 
R.3 | Coal share/import |  |  |  |  |  |  |  |  |  | 
R.4 | CO2 emissions |  |  |  |  |  |  |  |  |  | 
R.5 | LCOE |  |  |  |  |  |  |  |  |  | 
R.6 | Reserve margin |  |  |  |  |  |  |  |  |  | 
R.7 | Renewable energy share |  |  |  |  |  |  |  |  |  | 
R.8 | Total investment cost |  |  |  |  |  |  |  |  |  | 

## Slide 8: Population growth rate of Vietnam

## Slide 9
Back - casting of Power demand of Vietnam
Historical Power Demand

## Slide 10
Back - casting of Power demand of Vietnam
Power development plan VI

## Slide 11
Back - casting of Power demand of Vietnam
Power development plans VII and VII Rev.

## Slide 12
Comparison of Power demand projection
Other scenarios

## Slide 13: Costs of electricity generation technologies

## Slide 14: Energy Models used in the scenarios reviewed

## Slide 15
Comparison of Generation mix in 2030

## Slide 16
Comparison of Generation mix in 2030

## Slide 17
Comparison of Capacity mix in 2030

## Slide 18: Installed power capacity

## Slide 19
Comparison of the share of coal in 2030
More renewable energies and energy efficiency strategy provide solution to import less coal

## Slide 20
Comparison of CO2 emissions
Vietnam NDC 1
GHG emissions in 2030
787.4 Mt CO2 e
From Energy sector
675.4 Mt CO2 e
Domestic support
645.9 Mt CO2 e
International support
638.9 Mt CO2 e
Source: Viet Nam’s Intended Nationally Determined Contribution

## Slide 21
Comparison of CO2 emissions in 2030

## Slide 22: Carbon’s price
For carbon’s price, most of scenarios based on the price proposed the estimated CO2 externality value in Vietnam: 7 USD/ton for near term projection and 20 USD/ton thereafter for long term projection S
Some exceptional cases are: (i) 20 USD/ton was set for the whole modelled period by WWF (2016) scenarios [6], or (ii) 35 USSD/ton (taken from IMF 2014 source) in the GreenID (2017) study [7], or
(iii) Danish Energy Agency (2017) – CO2 price high scenarios investigated to an ambitious environmental policies by imposing the most highest CO2 price: the starting price at 20 USD/ton in 2020, achieving 45 USD/ton in 2035 and being constant until 2050.

## Slide 23
Conclusion
High dependency on non-renewable fuel such as crude oil, natural gas and coal as sources of energy (53 GW from coal power plants in 2030 – PDP7 rev) from official power development plans. Other alternatives provide brighter perspectives
It is possible for Vietnam to achieve the commitment of the government to reduce 8% and 25% of GHG emissions without and with international supports, if Vietnam goes for green scenarios
Renewable energies are not yet utilized to their maximum potential in Vietnam due to high costs and insufficient market conditions
Challenges for energy transitions: RE grid integration, investment for clean power generation, soci0-economic and environmental impacts, etc.

## Slide 24
Thank you for your attention